## Slide 1: Lab 01 programming an stm32 arm coretex-m 32-bit microcontroller
Prof. Davide Brunelli
Dept. of Industrial Engineering – DII
University of Trento, Italy
davide.brunelli@unitn.it

## Slide 2
Plan a: Accessing the virtual machine

## Slide 3
Plan b: running the software natively

## Slide 4: Stm32 development environment
Download the archive from
https://drive.google.com/drive/u/2/folders/1tHQ5O4eaGEEBfe2oR7O2w1nYTZAlRr4r
Unzip it

## Slide 5: Stm32 development environment
Install the 3 software following the order
  Java Runtime Environment
  System Workbench
  STM32 Cube-MX
Finally, download MobaXterm from https://mobaxterm.mobatek.net/download.html
Java Runtime Env.
System Workbench
STM32 Cube-MX

## Slide 6
STM32 NUCLEO L4

## Slide 7: STM32 NUCLEO FAMILY
  Ideal for quick prototyping
  Standardized connectivity, reusable across all Nucleo boards
  Extends connectivity even to Arduino boards
  Each board contains an ST-LINK in-circuit debugger and programmer (usable even for external applications compatible with STM32 MCUs)

## Slide 8: STM32 NUCLEO f401re
ST-LINK
(programmer)
STM32 NUCLEO BOARD

## Slide 9: STM32 NUCLEO f401re

## Slide 10: STM32 NUCLEO f401re

## Slide 11: STM32 NUCLEO f401re

## Slide 12
Stm32 cubemx

## Slide 13: Stm32 cubemx – selecting the board
A graphical tool which enables fast configuration of STM32 microcontrollers and microprocessors.
Generates the corresponding C code for the Arm Coretex core.

## Slide 14: Stm32 cubemx – selecting the board

## Slide 15: Stm32 cubemx – multiplexing the pins
Selected pins are preassigned, since we are using a development board, with predefined connections

## Slide 16: Stm32 cubemx – setting the clocks
CLOCK
SOURCE
CPU FREQ
PERIPHERAL CLOCK
Clock tab allows us to configure the clock. Here you can select your clock source, the CPU frequency and the peripheral clock

## Slide 17: Stm32 cubemx – configuring the peripherals
System view tab allows us to configure all the peripheral. As you activate the peripheral from “Pinout” tab, those will be added here

## Slide 18: Stm32 cubemx – setting the toolchain
Change the toolchain / IDE to system workbench
Once everything is configure, we can generate the code

## Slide 19
Systemworkbench
for stm32

## Slide 20: Stm32 – system workbench

## Slide 21: Stm32 – system workbench
main.c -> Main file
stm32f4xx_it.c -> Interrupt service routine
stm32f4xx_hal_msp.c -> HAL library initialization
system_stm32f4xx.c -> System low level config

## Slide 22: Stm32 – system workbench
If you are using a virtual machine, before building and compiling, be sure to have enabled the STM board as a USB Device

## Slide 23: Stm32 – system workbench
We can build the code pressing the hammer icon, while for executing it inside our development platform, press the green arrow

## Slide 24: Stm32 – system workbench
If you do not have any available options on the “Run as” menu, right click on your project folder and try a “Refresh”.
If the issue still appears, try with “Clean Project”, rebuild it and refresh it.

## Slide 25: Additional material
MCU Datasheet
  http://www.st.com/content/ccc/resource/technical/document/datasheet/30/91/86/2d/db/94/4a/d6/DM00102166.pdf/files/DM00102166.pdf/jcr:content/translations/en.DM00102166.pdf
STM32 Nucleo-64 User manual
  http://www.st.com/content/ccc/resource/technical/document/user_manual/98/2e/fa/4b/e0/82/43/b7/DM00105823.pdf/files/DM00105823.pdf/jcr:content/translations/en.DM00105823.pdf