## Slide 1
Lab 03 timers
Prof. Davide Brunelli
Dept. of Industrial Engineering – DII
University of Trento, Italy
davide.brunelli@unitn.it

## Slide 2
TIMERS

## Slide 3: Timers
3
A hardware timer is essentially an independent counter that counts from zero to its maximum value at a given speed and generates various events. It runs in the background independently from your C/C++ program and its value typically follows the sequence depicted below:
It is basically a global variable (timer counter) that increments (or decrements) on the basis of a programmable clock source

## Slide 4: Timers
4
The hardware of a timer is composed of three basic programmable parts:
The clock source: the circuit that generates the clock tick for the timer
The time base: the circuit that derives the time granularity from the clock source and contains the timer counter variable
The slave circuits: provide additional functions (pulse measure, signal generation, etc.) by exploiting the timer variable

## Slide 5: Timers
5
The STM32 MCU offers up to 11 different timer/counters with the following features:
Clock selection (internal, external, other)
16/32-bit counter resolution
Programmable prescaler
Four independent channels configurable as:
  Input Capture
  Output Compare
  PWM Mode
  One-pulse Output
Interrupt generation on the basis of the various events that can occur

## Slide 6: Timers
6
Counting is handled in the time-base by the following registers:
TIMx->PSC: the prescaler register; it directly specifies the division factor
TIMx->CNT: the counter register; it holds the counter value and increments (or decrements) it according to the input clock
TIMx->ARR: the auto-reload register; CNT counts from 0 to ARR, then CNT is set to 0 again
When CNT is reloaded, an update event is generated (the “U” in figure) which can trigger an interrupt generation

## Slide 7: STM32 Timers
7
The STM32 embeds multiple timers providing timing resources for software or hardware tasks.
The software tasks mainly consist of providing time bases, timeout event generation and time-triggers.
The hardware tasks are related to I/Os: the timers can generate waveforms on their outputs, measure incoming signal parameters and react to external events on their inputs.

## Slide 8: STM32 Timers
8
We will use TIM6 for our board.
TIM6 is a simple Timer acting as a Counter. It just counts the clock cycles up to the maximum value set and then reset.

## Slide 9: STM32 Timers
9
Timer tick time (or timer resolution) is base on APBx clock. It can be scaled using a 16 Bit prescaler. We can modify the base clock, to simplify the pre-scaler division.

## Slide 10: STM32 Timers
10

## Slide 11: STM32 Timers – Interrupt
11
We can activate the interrupt using the NVIC configuration tab in CubeMX

## Slide 12: STM32 Timers – Interrupt
12
Once the timer has reached its counting period, an interrupt will be fired. Using the proper callback function we can create timed tasks (like the blinking of a LED)
After the Peripheral Initializations, remember to start TIM6 In Interrupt Mode.

## Slide 13: STM32 Timers – Resources
13
General-purpose timer cookbook for STM32 microcontrollers
  https://www.stmicroelectronics.com.cn/content/ccc/resource/technical/document/application_note/group0/91/01/84/3f/7c/67/41/3f/DM00236305/files/DM00236305.pdf/jcr:content/translations/en.DM00236305.pdf
STM32L4 Timers
  https://www.st.com/content/ccc/resource/training/technical/product_training/c4/1b/56/83/3a/a1/47/64/STM32L4_WDG_TIMERS_GPTIM.pdf/files/STM32L4_WDG_TIMERS_GPTIM.pdf/jcr:content/translations/en.STM32L4_WDG_TIMERS_GPTIM.pdf

## Slide 14
TOGGLE THE LED
USING A TIMER

## Slide 15: TOGGLE THE LED USING A TIMER
15
Use the previously configured timer to toggle the green LED every 1 second.
Use CubeMX to configure a simple timer
Configure the board clock to provide an APB clock equal to 60 MHz
If needed, pre-scale the clock to a suitable frequency for the timer
Set the timer counting period
Start the timer using the blue button
Using the interrupt callback, toggle the green LED

## Slide 16
CHANGE THE TIMER COUNTING PERIOD

## Slide 17: CHANGE THE TIMER COUNTING PERIOD
17
Using an interrupt generated by an external input, cycle the timer counting period between 0 – 0.25s – 0.5s – 1s – 2s
Use CubeMX to configure a simple timer
Configure the board clock to provide an APB clock equal to 60 MHz
If needed, pre-scale the clock to a suitable frequency for the timer
Set the timer counting period
Using the interrupt callback, cycle the counting period of the configured timer by updating the relative register.