## Slide 1
Lab 05 USART & ADC
Prof. Davide Brunelli
Dept. of Industrial Engineering – DII
University of Trento, Italy
davide.brunelli@unitn.it

## Slide 2: USART
USART

## Slide 3: STM32 USART
3
Universal synchronous and asynchronous receiver-transmitter (USART) is a type of serial interface device that can be programmed to communicate asynchronously or synchronously.
The serial communication in asynchronous mode is one of the simplest and most used methods to exchange data between a microcontroller and other devices.

## Slide 4: STM32 USART
4
STM32 MCUs provide USART communication. We can communicate with the Nucleo board by activating USART peripheral. First you need a serial terminal, like MobaXterm. If necessary, download the software from -> https://mobaxterm.mobatek.net/download.html

## Slide 5: STM32 USART
5
Nucleo boards directly connect USART RX/TX pins to the mini USB port integrated in the STLink
PA2 = TX
PA3 = RX

## Slide 6: STM32 USART
6
USART parameters can be configured as always using CubeMX. In our case, we can stick with the default parameters.

## Slide 7: STM32 USART
7
Once everything is configure, we can generate the code. CubeMX will create the new configuration methods with all the parameters set using CubeMX
We can then transmit messages using the “HAL_UART_Transmit” function

## Slide 8
Send a message when button is pressed

## Slide 9: Send a message when button is pressed
9
Use the previously configured USART to send a message each time the pushbutton is pressed.
Use CubeMX to configure the pushbutton interrupt
Send “Hello from STM32” when such interrupt is triggered

## Slide 10: ADC
ADC

## Slide 11: SAR ADC
11

## Slide 12: STM32 ADC
12
STM32 boards provide one, or multiples, ADCs connected to different channels, each one consisting of a 12-bit successive approximation A/D converter.
Among all, ADC1 provides two channels internally connected to a temperature sensor and to Vref.

## Slide 13: STM32 ADC
13
As for the other peripherals, CubeMX let us configure the ADC in a graphical way.

## Slide 14: STM32 ADC
14
Once generated the code, the ADC configuration can be found inside the MX_ADC1_Init function

## Slide 15: STM32 ADC
15
The ADC routine provides us the binary representation of the voltage sensed. Before having human readable numbers, we have to convert the raw data coming from the ADC.
We can create a simple method named get_ADC(), that takes care of starting the ADC, retrieve the value and then stops the ADC. The value returned can later be converted to a voltage value using the following formula(referenced to 3.3 V)

## Slide 16: STM32 ADC
16
Once we have converted the ADC raw value, we have to convert this voltage to a Celsius value. MCU datasheet provides the parameters and the formula for conversion.
Vref and Avg_Slope must be defined accordingly !

## Slide 17: Exercise 8
Send temperature readings through usart

## Slide 18: Send temperature readings through usart
18
Use the previously configured USART and ADC as temperature sensor channel, send temperature readings through USART.
Use CubeMX to configure the USART
Use CubeMX to configure the ADC as temperature sensor channel
Send temperature readings through USART every 5 seconds.

## Slide 19: Exercise 9
Visual thermometer

## Slide 20: Visual thermometer
20
Starting from the last exercise, adjust the brightness of the led proportionally to the temperature readings.
Use CubeMX to configure the USART
Use CubeMX to configure the ADC as temperature sensor channel
Send temperature readings through USART every 5 seconds.
PLUS: adjust the led brightness proportionally to the temperature readings. [E.g. 25% if T < 20, 50% if 20 <= T <= 22 and 100% if T > 22]