## Slide 1
Lab 09 THE CONSOLE
Prof. Davide Brunelli
Dept. of Industrial Engineering – DII
University of Trento, Italy
davide.brunelli@unitn.it

## Slide 2: STM32 USART
2
Nucleo boards directly connect USART RX/TX pins to the miniUSB port integrated in the STLink
PA2 = TX
PA3 = RX

## Slide 3: STM32 USART
3
Check that the USART2 is enabled.

## Slide 4: STM32 Console
4
Enable the USART interrupt.
Remember to double check under “code generation” if IRQ generation is enabled

## Slide 5: STM32 Console
5
Once everything is configured and the code generated, we have to add the callback called when the USART receive a character.
In the callback, we take care of echoing back user input and storing it inside a buffer (defined as global variables).
#define MAXBUFFSIZE 100
uint8_t RxBuf [MAXBUFFSIZE];
uint8_t TxBuf [MAXBUFFSIZE];
void HAL_UART_RxCpltCallback(UART_HandleTypeDef *huart){
if(RxBuf[0] == '\r’){ // Check new line
HAL_UART_Transmit(&huart2, (uint8_t *)"\r\n", sizeof("\r\n"),10);
//cmd_check(); //TO BE IMPLEMENTED!!
}
else if(RxBuf[0] == '\b’){ //Check back space
HAL_UART_Transmit(&huart2, (uint8_t *)"\b \b", sizeof("\b \b"),10);
TxBuf[--char_counter] = NULL;
}else{ //Otherwise store inside our buffer
TxBuf[char_counter++] = RxBuf[0];
HAL_UART_Transmit(&huart2, (uint8_t *) RxBuf, sizeof(RxBuf),10); //Echoing
}
HAL_UART_Receive_IT(&huart2 , RxBuf, 1); // Restart UART in Interrupt mode
}

## Slide 6: STM32 Console
6
Finally start the UART in interrupt mode.

## Slide 7: ADC
CONSOLE – INTERACT WITH THE EMBEDDED SYSTEM

## Slide 8: 6d orientation estimator
8
Create a console program, that recognize a set of commands and execute them on
board.
Switch LED ON and OFF
Toggle LED
Start LED blinking
Get internal temperature
Hint: you can use strcmp((char *)TxBuf, command) to compare two strings